TECHNICAL DATA SHEET

Pigment Yellow 109

- Product Name

Trade Name: IsoINDOLINE Yellow 2RLT

C.I.: Pigment Yellow 109

C.I. No.: 56284

CAS No.: 5045-40-9

Molecular Formula: C23H8CL8N4O2

Formula Weight: 655.96

2. Physical, Chemical and Resistance Properties

Appearance: Yellow Powder

Shade: Similar to Standard

Moisture: ≤1.5

Fineness(80 Mesh): ≤5.0

PH Value: 7

Water Soluble Matter (%): ≤2.0

Oil Absorption (ml/100g): ≤50

Electric Conductivity (us/cm): ≤500

Acid Resistance: 5

Alkali Resistance: 5

Water Resistance: 5

Oil Resistance: 5

Heat Resistance (℃): 200

Light Fastness (8=excellent): 7

3. Application

Application:plastic,water-base coating, solvent-base coating,

water-base ink,solvent-base ink,offset ink

4．Packing

Packed in 25kgs Bag with Pallet.