TECHNICAL DATA SHEET

Pigment Red 48:1

1.Product description

Trade Name: Fast Scarlet 2BN

Color Index Pigment Red 48:1

C.I. No. 15865:1

CAS No. 7585-41-3

Chemical Formula: C18H11ClN2O6SBa

Molecular Weight: 556.16

Chemical Group BONS Ba

2. Physical, Chemical and Resistance Properties

Appearance: Red Powder

Shade: Similar to Standard

Tinting Strength:100%

Bulk Density(lb/gal): 12.4-17.4

Moisture: ≤1%

Oil Absorption: 40±5

Fineness(80 Mesh): ≤5%

PH Value: 6.5-9.0

Water Soluble Matter (%) ≤1.5

Oil Absorption (ml/100g) 40±5

Electric Conductivity (us/cm) ≤500

Acid Resistance 5

Alkali Resistance 4

Water Resistance: 5

Oil Resistance: 5

Alcohol Resistance 5

Ester Resistance 4

Benzene Resistance 4

Ketone Resistance 4

Soap Resistance -

Bleeding Resistance -

Migration Resistance 5

Heat Resistance (℃) 200

Light Fastness (8=excellent) 6

3. Application

Application: plastic

Recommended Application: Printing, water-base ink,solvent-base ink,offset ink

4．Packing

Packed in 25kgs Bag with Pallet.